## Slide 2
Team Member 1: Sharafathusein Kothariya(92301703020) (6EC1)
Team Member 2: Shubhra Gupta (92301703015) (6EC1)
Team Member 3: Anuska Singh (92301703037) (6EC1)
Mini Project (01CE0609)
Semester 6
Final Review 11/04/2026
Hourly Power Consumption For a Smart Home Using Time Series Models
Team ID: T_020
Guided By
Internal Guide
Prof. Ronak Doshi
Assistant Professor
Department of Computer Engineering, Faculty of Engineering & Technology

## Slide 3: Outline
Abstract
Objectives
Dataset Description
Data Preprocessing & Feature Engineering
Methodology & System Architecture
Literature Review
Research Gap
Model Architectures (LSTM, GRU, RF, GBM, Hybrid LSTM+GBM)
Model Training & Hyperparameters
Results & Performance Comparison
Conclusion & Future Work
References

## Slide 4: Abstract
The rapid growth of energy forecasting technologies has intensified the need for accurate and efficient power consumption management. This project presents a systematic comparative study of five time series forecasting models applied to the publicly available New York Independent System Operator (NYISO) hourly electricity load dataset. The models evaluated are Long Short-Term Memory (LSTM), Gradient Boosting Machine (GBM), Gated Recurrent Unit (GRU), a Hybrid LSTM+GBM ensemble, and Random Forest (RF). Evaluation metrics used are RMSE, MAE, MAPE, and R². The Hybrid LSTM+GBM model achieves the best performance: RMSE of 52.50 MW, MAE of 35.43 MW, MAPE of 0.60%, and R² of 0.9979, representing a 40.3% improvement in RMSE over the GRU baseline. The study confirms that combining the sequential temporal learning of LSTM with the residual error correction strength of GBM yields a highly accurate forecaster for intelligent energy grid management.

## Slide 5: Objectives
Conduct exploratory data analysis (EDA) on the NYISO hourly electricity load dataset, identifying diurnal, weekly, and seasonal patterns.
Design and implement a comprehensive data preprocessing pipeline handling missing values, outliers, duplicate timestamps, and feature engineering.
Implement and train five time series forecasting models - LSTM, GBM, GRU, Hybrid LSTM+GBM, and Random Forest under identical experimental conditions.
Evaluate all five models on a held-out test set using RMSE, MAE, MAPE, and R² metrics.
Identify the best-performing model and provide architectural explanations for its superiority.
Derive practical insights for deploying the identified model in intelligent energy grid management systems.

## Slide 6: Dataset Description
Dataset Source
New York Independent System Operator (NYISO) — Hourly Integrated Real-Time Actual Load data
Publicly available at https://www.nyiso.com/load-data — no licence fees required
5 years of hourly data consolidated → ~43,800 observations (state-wide aggregate)
Dataset Characteristics
Fields: Timestamp (Eastern Time), Zone name, Load value (MWh)
Diurnal pattern: Peak demand 17:00–20:00; nadir 03:00–05:00
Weekly pattern: Weekday consumption 8–12% higher than weekends
Seasonal pattern: Summer peak (cooling load) + secondary winter peak (heating)
Distribution: Mean ≈ 17,500 MW, SD ≈ 3,200 MW, slight positive skewness (0.35)

## Slide 7: Data Preprocessing & Feature Engineering
Preprocessing Pipeline (5 Steps)
Step 1 - Data Ingestion: Monthly CSV files loaded via pandas; timestamp parsed to datetime
Step 2 - Missing Values: Linear interpolation for short gaps (1–3 hrs); forward-fill for single-hour gaps
Step 3 - Duplicate Timestamps: DST fall-back duplicates resolved by averaging the two load values
Step 4 - Outlier Detection: 168-hr rolling z-score; |z| > 3.0 → linear interpolation (~0.3% of records)
Step 5 - Normalisation: MinMaxScaler fitted on training set only; applied to validation & test sets
Feature Engineering - 14 Input Features
Temporal (5): hour_of_day, day_of_week, day_of_month, month, is_weekend
Lag features (7): lag_1h, lag_2h, lag_3h, lag_6h, lag_12h, lag_24h, lag_168h
Rolling statistics (2): rolling_mean_24h, rolling_std_24h
Dataset split: Training 70% | Validation 15% | Test 15% (chronological — no data leakage)

## Slide 8: Methodology - System Architecture
System Architecture - Five-Stage Modular Diagram

## Slide 9: Methodology - System Architecture
System Architecture - Five-Stage Modular Diagram
► Stage 1: DATA INGESTION - Load & consolidate NYISO monthly CSV files; parse timestamps
↓
► Stage 2: DATA PREPROCESSING - Missing values, DST duplicates, outlier replacement, normalisation
↓
► Stage 3: FEATURE EXTRACTION & SPLITTING - 14 features; 70/15/15 chronological split; 3D tensors for DL, 2D for ML
↓
► Stage 4: MODEL TRAINING - LSTM | GRU | GBM | Random Forest | Hybrid LSTM+GBM (early stopping, fixed seed=42)
↓
► Stage 5: MODEL VALIDATION - RMSE, MAE, MAPE, R² on held-out test set; forecast-vs-actual plots

## Slide 10: Literature Review
Statistical Approaches - The Baseline
Early forecasting methods relied on ARIMA and SARIMA models. While effective for linear, stable demand patterns [6][7], these statistical approaches fundamentally fail to capture the nonlinear, multi-scale periodicities of real-world hourly grid data, motivating the shift toward machine learning.
Machine Learning - Handling Nonlinearity
Tree-based ensemble methods emerged as a strong alternative. Bilal et al. [8] showed that Gradient Boosting and Random Forest offer the best accuracy-efficiency trade-off for energy data.

## Slide 11: Literature Review
Deep Learning - Capturing Temporal Dependencies
LSTM networks [10] overcame the vanishing gradient problem of standard RNNs, enabling long-range sequence learning. Qureshi et al. [9] confirmed LSTM substantially outperforms ARIMA on electricity demand.
Hybrid Models - The Current Frontier
Recent studies combine multiple paradigms for superior results. Hammou Ou Ali et al. [12] proposed a CNN-RNN hybrid for energy forecasting. Ngo et al. [22] demonstrated SARIMA-SVR for building energy.
Critical Gap Identified
No prior work performs a unified comparison of deep learning, ensemble ML, and a two-stage LSTM+GBM hybrid on the same hourly grid dataset under consistent experimental conditions - which this project directly addresses.

## Slide 12: Research Gap
No comprehensive comparative evaluation of heterogeneous model families (DL + ML ensemble + hybrid) on the same electricity load dataset under unified experimental conditions exists in prior literature.
Classical statistical models (ARIMA, SARIMA) cannot capture nonlinear, multi-scale periodicities in real-world hourly grid data.
Existing ML models deployed in isolation — no systematic benchmark against deep learning or hybrid architectures.
A two-stage hybrid combining LSTM’s temporal learning with GBM’s gradient-based residual correction for hourly grid-level forecasting had not been previously explored.
Evaluation protocols in published studies are inconsistent — different datasets, split strategies, and metrics prevent direct comparison.
This Project Addresses:
Unified five-model comparison on NYISO data under identical conditions with fixed random seed (42)
Novel Hybrid LSTM+GBM two-stage architecture as principal research contribution

## Slide 13: Model Architecture - LSTM
Long Short-Term Memory (LSTM)
LSTM networks maintain a cell state cₜ alongside hidden state hₜ, updated through three gates: forget gate (what to discard), input gate (what to write), and output gate (what to expose). This prevents vanishing gradient degradation across long sequences.
Architecture & Hyperparameters
2 stacked LSTM layers: 128 units → 64 units
Dropout = 0.2 after each layer (regularisation)
Dense output layer: 1 unit (hourly load prediction)
Optimiser: Adam (lr = 0.001) | Loss: MSE
Batch size: 64 | Max epochs: 100
Early stopping: patience = 10 (monitor val_loss)
Input: 3D tensor (samples, 24, 14) — 24-hour lookback window
Test Performance: RMSE = 78.34 MW | MAE = 58.22 MW | MAPE = 1.03% | R² = 0.9954

## Slide 14: Model Architecture - GRU
Gated Recurrent Unit (GRU)
GRU simplifies LSTM by combining the forget and input gates into a single update gate zₜ and introducing a reset gate rₜ. This reduces trainable parameters by ~25% vs. equivalent LSTM while maintaining comparable temporal modelling capacity.
Architecture & Hyperparameters
2 stacked GRU layers: 128 units → 64 units
Dropout = 0.2 after each layer
Dense output layer: 1 unit
Optimiser: Adam (lr = 0.001) | Loss: MSE | Batch: 64
Early stopping: patience = 10 (val_loss) | Max epochs: 100
Input: 3D tensor (samples, 24, 14) — same as LSTM for fair comparison
Test Performance: RMSE = 87.98 MW | MAE = 63.85 MW | MAPE = 1.10% | R² = 0.9941 (Deep learning baseline)

## Slide 15: Model Architecture - Random Forest
Random Forest (RF)
Random Forest constructs n_estimators independent decision trees on bootstrap samples, with feature subsampling (max_features = sqrt) at each split to decorrelate trees. The final prediction is the average of all tree outputs.
Architecture & Hyperparameters
n_estimators = 300 | max_depth = None (full depth)
min_samples_split = 2 | max_features = sqrt
bootstrap = True | random_state = 42
Input: 2D feature matrix (samples, 14)
Feature importance (Gini) extracted for interpretability
Test Performance: RMSE = 72.94 MW | MAE = 51.04 MW | MAPE = 8.87% | R² = 0.9960

## Slide 16: Model Architecture - GBM
Gradient Boosting Machine - GBM
GBM iteratively adds decision tree estimators, each trained to predict the negative gradient (residuals) of the current ensemble’s loss. This additive residual correction is also the theoretical foundation for the Hybrid model.
Architecture & Hyperparameters
n_estimators = 500 | max_depth = 6
learning_rate = 0.05 | subsample = 0.8 | colsample_bytree = 0.8
reg_lambda = 1 | Early stopping: 50 rounds on validation RMSE
Input: 2D feature matrix (samples, 14)
Test Performance: RMSE = 62.70 MW | MAE = 43.97 MW | MAPE = 0.75% | R² = 0.9954
14% RMSE improvement over Random Forest. Gradient-boosted residual learning effectively captures nonlinear lag/calendar feature relationships.

## Slide 17: Model Architecture - Hybrid LSTM+GBM
Hybrid LSTM+GBM - Novel Contribution
The Hybrid model employs a two-stage architecture that decomposes forecasting into temporal pattern modelling (LSTM) and residual error correction (GBM). This is the principal novel contribution of this project.
Two-Stage Design
Stage 1 (Temporal Modelling): Train LSTM to convergence on training set.
Stage 2 (Residual Correction): Train GBM on residuals using same 2D feature matrix.
Why It Works
LSTM captures long-range sequential dependencies in time-indexed data
GBM corrects systematic feature-driven errors that LSTM cannot capture alone
Test Performance: RMSE = 52.50 MW | MAE = 35.43 MW | MAPE = 0.60% | R² = 0.9979

## Slide 18: Model Training & Hyperparameters
Training Environment
Platform: Google Colab with NVIDIA T4 GPU (15 GB VRAM)
GPU reduces LSTM/GRU training time from ~4 hrs (CPU) to <20 min per model
Stack: Python 3.10.12 | TensorFlow 2.12.0/Keras | XGBoost 1.7.6 | Scikit-learn 1.2.2
Fixed random seed (numpy=42, tensorflow=42) for full reproducibility

## Slide 19: Results - Forecast vs. Actual Load
Forecast vs. Actual Load - 500-Hour Test Window
GRU: RMSE = 87.98 MW - Captures overall diurnal trend but shows moderate deviation at peak demand hours. Highest error among all models.

## Slide 20: Results - Forecast vs. Actual Load
Forecast vs. Actual Load - 500-Hour Test Window
LSTM: RMSE = 78.34 MW - Improved peak/trough tracking vs. GRU. Cell state mechanism retains long-range temporal context across full window.

## Slide 21: Results - Forecast vs. Actual Load
Forecast vs. Actual Load - 500-Hour Test Window
Random Forest: RMSE = 72.94 MW, R² = 0.9960 - Follows general load trend well but under-predicts at peak demand; elevated MAPE (8.87%) from overnight low-load periods.

## Slide 22: Results - Forecast vs. Actual Load
Forecast vs. Actual Load - 500-Hour Test Window
GBM: RMSE = 62.70 MW - Tighter peak alignment than RF and LSTM. Gradient-boosted residual learning effectively captures nonlinear lag/calendar relationships.

## Slide 23: Results - Forecast vs. Actual Load
Forecast vs. Actual Load — 500-Hour Test Window
Hybrid LSTM+GBM: RMSE = 52.50 MW, R² = 0.9979 - Tightest alignment with actual load curve across entire 500-hour window. Best across all four metrics.

## Slide 24: Performance Comparison
Performance Comparison - All Five Models
Key Improvements of Hybrid LSTM+GBM
vs. standalone LSTM: 33.0% RMSE reduction, 41.6% MAPE reduction
vs. standalone GBM: 16.3% RMSE reduction, 19.9% MAPE reduction
vs. GRU baseline: 40.3% RMSE reduction
R² = 0.9979 → 99.79% of test set variance explained

## Slide 25: Result Analysis & Discussion
Key Findings
GRU establishes the deep learning baseline (RMSE 87.98 MW, MAPE 1.10%). Simpler gating vs. LSTM results in higher error.
LSTM outperforms GRU (RMSE 78.34 MW) - long-range cell state mechanism is beneficial for 24-hour lookback sequences.
Random Forest achieves strong R² (0.9960) but elevated MAPE (8.87%) from near-zero overnight load values. Disqualified for % error-sensitive applications.
GBM outperforms RF by 14% in RMSE (62.70 MW) and achieves MAPE of 0.75% — gradient-boosted residual learning superior over bagging with structured features.
Hybrid LSTM+GBM achieves best across all four metrics — validating the hypothesis that LSTM temporal learning and GBM residual correction are genuinely complementary.
System-Level Acceptance Criteria — All Met
RMSE < 60 MW → Achieved: 52.50 MW ✓
MAPE < 1.0% → Achieved: 0.60% ✓
R² > 0.995 → Achieved: 0.9979 ✓

## Slide 26: Conclusion & Future Work
Summary
Systematic comparison of 5 heterogeneous forecasting models under unified experimental conditions on the NYISO dataset.
Hybrid LSTM+GBM confirmed as optimal: RMSE = 52.50 MW, R² = 0.9979 (40.3% RMSE reduction over GRU baseline).
Full technical viability demonstrated using open-source tools and a public dataset within 12-week semester at zero cost.
Limitations
NYISO regional aggregate data - not sub-metered appliance-level data
No exogenous weather variables incorporated (temperature, humidity, irradiance)
Offline batch training - not deployed for real-time inference on live grid streams
Future Enhancements
Multi-region validation: More datasets to be trained including India’s POSOCO dataset
Integrate exogenous weather API feeds

## Slide 27: References
[1] Grand View Research, “Smart home market size, share & trends analysis report,” Grand View Research, 2023.
[2] S. Haben et al., “Analysis and clustering of residential customers energy behavioral demand using smart meter data,” IEEE Trans. Smart Grid, vol. 7, no. 1, pp. 136-144, 2016.
[3] J. Kelly & W. Knottenbelt, “The UK-DALE dataset,” Scientific Data, vol. 2, p. 150007, 2015.
[4] R. Weron, “Electricity price forecasting: a review of the state-of-the-art,” Int. J. Forecasting, vol. 30, no. 4, pp. 1030-1081, 2014.
[5] D. P. Chassin et al., “GridLAB-D: an open-source power systems modeling environment,” IEEE PES T&D, 2008.
[6] Gopikrishna P.B. et al., “Power consumption prediction using ARIMA,” IEEE Int. Conf. Advances in Computing, 2021.
[7] P.K. Jain et al., “Electricity consumption forecasting using time series analysis,” Int. Conf. IT, 2018.
[8] M. Bilal et al., “Comparative analysis of energy forecasting models,” Sustainability, vol. 14, 2022.
[9] A. Qureshi et al., “LSTM electricity prediction for smart homes,” Sustainability, vol. 16, 2024.
[10] S. Hochreiter & J. Schmidhuber, “Long short-term memory,” Neural Computation, vol. 9, no. 8, pp. 1735-1780, 1997.
[11] M.T. Ucar & A. Kaygusuz, “Short-term energy forecasting using deep learning models,” Energy Reports, vol. 11, 2025.
[12] I. Hammou Ou Ali et al., “Predicting short-term energy usage in smart home using hybrid DL models,” Frontiers in Energy Research, vol. 12, 2024.
[13] K. Ullah et al., “Short-term load forecasting using CNN-LSTM,” IEEE Access, vol. 12, 2024.
[14] B. Devanathan et al., “AI-based energy consumption forecasting in smart homes,” IEEE, 2025.

## Slide 28: References
[15] F. Dewangan et al., “Load forecasting models in smart grid using smart meter information,” Energies, vol. 16, 2023.
[16] NYISO, “Hourly integrated real-time actual load data,” [Online]. Available: https://www.nyiso.com/load-data
[17] J.G.A. Caw-it & F.J.B. Talirongan, “Forecasting household electricity using ARIMA,” IEEE, 2025.
[18] A. Banga et al., “Stacking ML models for electricity forecasting,” IEEE, 2021.
[19] K. Alsalem, “Hybrid time series forecasting using fuzzy clustering & ML,” Applied Sciences, vol. 15, 2025.
[20] L. Wang et al., “Residential electricity forecast using temperature and deep learning,” Energy, vol. 290, 2025.
[21] B. Allehyani, “Hybrid CNN-LSTM and TimeGAN for smart home energy prediction,” IEEE Access, vol. 12, 2024.
[22] N.T. Ngo et al., “Hybrid AI model for building energy forecasting using SARIMA-SVR,” Energy and Buildings, vol. 255, 2022.
[23] B. Parizad et al., “Hybrid ML model for energy demand and price forecasting,” Sustainable Energy Tech., vol. 62, 2024.
[24] A. Rizwan et al., “Federated transfer learning for smart home energy prediction,” IEEE Access, vol. 12, 2024.
[25] M. Meyer et al., “Benchmarking time series models for electricity load forecasting,” Energy and AI, vol. 19, 2025.
[26] H. Kim et al., “Time-series clustering and forecasting of household electricity demand,” Energy Reports, vol. 9, 2023.
[27] T. Chen & C. Guestrin, “XGBoost: a scalable tree boosting system,” ACM SIGKDD, pp. 785-794, 2016.
[28] L. Breiman, “Random forests,” Machine Learning, vol. 45, no. 1, pp. 5-32, 2001.